## Slide 1: SENSOR(s) MEASUREMENT PROJECT MPU6050 Module DHT-11 Ultrasonic Water Level Detection
By: Lucas Scheibal, Lin Shen, Yiyang Chen, Cheng Chen and Iretomiwa Idowu

## Slide 2: MPU6050 Module
The MPU6050 is a multi-axis accelerometer and gyroscope that measures linear acceleration and angular acceleration respectively.
Working Principle
The accelerometer measures linear acceleration by using tiny systems to see how close to plates are to each other.
The gyroscope measures angular acceleration and it does this with a continuously oscillating mass and the known physics of the Coriolis effect.
2

## Slide 3: Range Resolution Important Characteristics
Sensitivity
Accuracy
Repeatability
Precision
Linearity
Specs Table/
Datasheet
Accelerometer ODR range | 8kHz to 1.25Hz
Accelerometer Range | ±2g, ±4g, ±8g, ±16g
Accelerometer sensitivity | at ±2g: 16384 LSB/g at ±4g: 8192 LSB/g at ±8g: 4096 LSB/g at ±16g: 2048LSB/g
Gyroscope ODR range | 8kHz to 1.25Hz
Gyroscope range | ± 250, ± 500, ± 1000, ± 2000 dps
Gyroscope sensitivity | at ±250dps: 131 LSB/dps at ±500dps: 65.5 LSB/dps at ±1000dps: 32.8 LSB/dps at ±2000dps: 16.4 LSB/dps
3

## Slide 4: Measurement Process
Gyroscope
Ground Truth- Determined angular velocity using supplied encoder
Assumed higher accuracy from encoder dur to counting instead of measuring
Measured in degrees per second
Accelerometer
Ground Truth - Utilized centripetal acceleration formula to find ground truth based on angular velocity
Measures in g’s
4

## Slide 5: More pictures of the testing Setup
Accelerometer Testing Setup
Gyroscope Testing Setup
5

## Slide 6
The goal was to obtain angular velocity of a drill at different points
Issues with encoder being unable to keep up
Issues with recreating speeds
Ground
Truth Value
Ground Truth Result
Ground Truth
Angular Velocity estimation of 37.1 counts/second
20 counts per rotation according to data sheet
6

## Slide 7
Accelerometer Results
Sensor Characteristics
Repeatability
  Measurements along Y axis
    1 inch: [-0.28g, -0.29g, -0.33g] with average of -0.30g, expected -0.35g
    2 inch: [-0.61g, -0.54g, -0.63] with average of -0.59g, expected -0.71g
    3 inch: [-0.84g, -0.92g, -1.13g] with an average of -0.96g, expected -1.05g
Range
  Unable to test due to wires
Sensitivity
  Expected
Resolution
  Needed to accurately control
7

## Slide 8
Summary of findings and Improvements
Use 12V motor and something like PWM to control angular velocity
  Verify with better encoder
Mount motor at exactly horizontal or vertical
Power Arduino without computer (battery)
Utilize onboard storage for results when set up is moving
8

## Slide 9: DHT-11 Module
The DHT-11 is a temperature and humidity sensor. It features a resistive-type humidity measurement component, a NTC temperature measurement component and an 8-bit microcontroller. Its primary purpose is to measure temperature and humidity.
Working Principle
The DHT11 sensor consists of a capacitive humidity sensing element and a thermistor for sensing temperature.
Important Characteristics and Specs Table
9

## Slide 10: Measurement Process and Ground Truth
As for how to measure, the method I choose is to use the car air conditioning, and because the car has a more accurate temperature sensor that could serve as the ground truth and thus can be compared with the temperature measured by the DHT-11 sensor. The characteristics I choose to measure are drift, static error and linearity. Therefore, there is no need to use a very low temperature, and the car air conditioning is fully competent for this job In the car, we can turn on the automatic mode of the air conditioner, and when the specified temperature is reached, the air conditioner will stop, and we can use the sensor to measure
Testing Setup
10

## Slide 11
Rundown of characteristics measurement process , Data collected , Findings and Analysis
11

## Slide 12
For drift, we put the sensor outside to measure the temperature of the day and check the temperature of the day according to the phone. And keep the sensor running for one minute ,we can get under data.
the temperature is still 11*C
19:58:54.085 -> Humidity: 66.50 Temperature: 10.20 *C
19:58:56.110 -> Humidity: 66.60 % Temperature: 10.20 *C
19:58:58.156 -> Humidity: 66.70 % Temperature: 10.20 *C
19:59:00.187 -> Humidity: 66.80 % Temperature: 10.20 *C
19:59:02.215 -> Humidity: 66.80 % Temperature: 10.20 *C
19:59:04.229 -> Humidity: 66.80 % Temperature: 10.20 *C
19:59:06.269 -> Humidity: 66.90 % Temperature: 10.10 *C
19:59:08.287 -> Humidity: 67.00 % Temperature: 10.10 *C
19:59:30.593 -> Humidity: 67.80 % Temperature: 9.90 *C
we can see that when we keep the input to be 11, but the measure temperature is still changing.
Drift
12

## Slide 13
Keep the temperature inside the car at () °C, then use DHT-11 to get the output, and compare with the vehicle thermometer reading, repeat for 3 groups
Static Error
13

## Slide 14
Linearity
For linearity, we adjust the temperature in the car to a certain value, then put the sensor in the car, and read a stable output after a period of time. Changing the temperature inside the car was repeated six times, and we chose to use MATLAB to draw the graph to observe whether it was linear
14

## Slide 15
Summary of Findings
Temperature adds up everywhere which is why the first time we tried measuring , our readings were off by a considerable amount which we did not know at that time was out body temperature
It took about 10 mins for the sensor to go from the previous temperature to the new temperature(this is where most of the lack of the sensor was coming from
The longer the sensor stayed at a temperature the more the drift!
15

## Slide 16: Water level Detection sensor
The Water Level Detection Sensor very self-descriptive as it does what it says it does: detect water level. It features ten copper wires in which 5 are sense traces and the remaining five are power traces
Working Principle
The sensor produces an output voltage proportional to the resistance; by measuring this voltage, the water level can thus be determined, measured and thus displayed!
Important Characteristics and Specs Table
Sensor Type | Analog
Detection Area | 40mm * 16mm
Operating temperature | 10℃-30℃ Humidity: 10% -90% non-condensing
16

## Slide 17: Measurement Process and Ground Truth
The ground truth was not only easily accessible but also easy to measure. We used a tape rule to measure and mark the ground truths of the length on transparent cup, we then went on to fill water to those levels and used the sensor to once again confirm the ground truth.
Testing Setup
17

## Slide 18
To measure the range, we submerged the sensor in water and gradually increase the depth until it no longer detected water. We then compared this to the range specified by the data sheet
Static Characteristics Measurement Process
To measure sensitivity, we slowly increased the water level while observing the sensor’s output. We did this till we obtained multiple readings, plotted it and then extracted the data we needed to quantify these characteristics
Sensitivity/Linearity
Range
As mentioned in the proposal, we tried to measure resolution, and to do this we tried making small incremental changes in water level and observing the corresponding changes in the sensor’s output. We found this really hard as the uncertainty was once again to high to ignore
To measure this, we obtained multiple readings at same water level (with the water level already premeasured) and then used Excel to calculate the standard deviation of the readings from each other and the ground truth.
Resolution
Precision, Accuracy and Repeatability
18

## Slide 19
Data collected, Findings and Analysis
Precision –Looking at the graph, all points overlap the ground truth
Repeatability – Again values overlap each other
Drift – 5 readings spread out within 1 mins
19

## Slide 20
Data collected, Findings and Analysis
Linearity R^2 = 0887. This shows that the graph is not as linear as we would want it to be but this is to be expected due to the fluctuations
Range –Accurate within the manufacture spec ( 1.6 - 4cm)
Resolution: Cannot be quantified due to the error we observed during testing
Sensitivity: Slope =47.467
20

## Slide 21
Comparison and Summary of Findings
From the data to the side, we can conclude a lot of things but the most important things we need to focus is that the data matches the data sheet especially the range
Water waves made the readings fluctuate before stabilizing which took about 20seconds decreasing the linearity of the sensor
 | Sensor Analog Readings |  |  |  |  |  |  |  | 
True Value(cm | 1 | 2 | 3 | 4 | 5 | Average | Std | Deviation | Error
1 | 554 | 553 | 553 | 554 | 554 | 553.6 | 0.547723 | 1 | 55260
1.5 | 585 | 584 | 584 | 584 | 585 | 584.4 | 0.547723 | 1 | 38860
2 | 600 | 597 | 597 | 596 | 597 | 597.4 | 1.516575 | 4 | 29770
2.5 | 612 | 612 | 610 | 610 | 612 | 611.2 | 1.095445 | 2 | 24348
3 | 625 | 625 | 625 | 625 | 625 | 625 | 0 | 0 | 20733.33
3.5 | 648 | 648 | 648 | 648 | 647 | 647.8 | 0.447214 | 1 | 18408.57
4 | 669 | 669 | 669 | 669 | 669 | 669 | 0 | 0 | 16625
4.5 | 755 | 754 | 754 | 755 | 754 | 754.4 | 0.547723 | 1 | 16664.44
21

## Slide 22: Ultrasonic Module
The HS-SR04 is a proximity sensor. It features two ultrasonic transducers. One is transmitter which outputs ultrasonic sound pulses and the other is receiver which listens for reflected waves. Its primary purpose is to measure distance
Working Principle
It uses the echo time method to detect the time of ultrasonic round trip to the measured distance.
Important Characteristics and Specs Table
Range | 2cm – 400cm (Practically 80cm)
Accuracy | ± 3mm
Resolution | 0.3cm
Sensitivity | -65dB min
22

## Slide 23: Measurement Process and Ground Truth
The ground truth was not only easily accessible but also easy to measure. We used a ruler and a tape rule at two different instances to measure the ground truth and then set up the sensor and an obstacle in a way that we could increase and decrease distance as needed. See below
Testing Setup
23

## Slide 24
First, we put the sensor and the object together, at which point the measurement distance is too small to be beyond the sensor‘s measurable range, so the readings are approximately infinite. Then we slowly move the object away until a recognizable reading appears, which we use as the minimum value of the sensor. Then we gradually move the object away from the sensor in units of 10cm, and when the reading shows infinity again, the description is beyond the maximum range, and then we gradually move the object closer to the sensor in 1cm units to find the critical point where the reading can be identified and the reading is approximately infinite. This distance was then considered the maximum value that the sensor can measure.
Static Characteristics measurement process
The sensor in different distance several times, The measured data was then averaged and compared with the actual distance. Then the measured distance and the actual distance are used as horizontal and vertical coordinates to plot their functions.
Sensitivity
Range
24

## Slide 25
We tried this by setting the sensor at a premeasured distance and with the ruler in between the sensor and the object, we tried adjusting the distance in increments of 0.1cm till we start getting a discernable output from the sensor. But the data was not reliable due to too much uncertainty which you can observe in the deviation
Quick run though of measurement process
For this we just took multiple readings of different distances, plotted the values against each other and extracted the data we needed to qualify and quantify these characteristics as can be seen in the next slide .
Accuracy, Precision Reliability
Resolution
25

## Slide 26
Data collected, Findings and Analysis
Accuracy/Precision –Looking at the graph, all points neglecting the outliers overlap the ground truth
Repeatability – Again values overlap each other
Drift – 10 readings spread out within 2 mins
26

## Slide 27
Data collected, Findings and Analysis
Linearity R^2 = 0.9999, Also the equation of the graph is linear
Range –Accurate within the manufacture spec (2 – 250cm)
Resolution: Cannot be quantified due to the error we observed during testing
Sensitivity: Slope = 0.9963
27

## Slide 28
Comparison and Summary of Findings
 | Sensor Readings |  |  |  |  |  |  |  |  |  |  |  |  | 
Ground Truth(cm | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | Average | Std | Deviation | % Error
0 | 1126.03 | 1126.07 | 1126.12 | 1126.19 | 1126.36 | 1126.91 | 1126.88 | 1126.17 | 1126.17 | 1126.03 | 1126.293 | 0.33143 | 0.88 | #DIV/0!
1 | 4.09 | 4.09 | 3.98 | 3.98 | 3.98 | 4.03 | 4.09 | 4.09 | 4.09 | 4.09 | 4.051 | 0.052377 | 0.11 | 305.1
2 | 2.88 | 2.76 | 2.88 | 2.86 | 2.86 | 2.88 | 2.88 | 2.86 | 2.78 | 2.86 | 2.85 | 0.043461 | 0.12 | 42.5
3 | 3.17 | 3.07 | 3.12 | 3.07 | 3.17 | 3.17 | 3.17 | 3.17 | 3.17 | 3.17 | 3.145 | 0.042492 | 0.1 | 4.833333
4 | 4.09 | 3.98 | 4.09 | 4.09 | 3.98 | 3.98 | 4.09 | 4.09 | 4.09 | 3.98 | 4.046 | 0.056804 | 0.11 | 1.15
5 | 4.59 | 4.69 | 4.71 | 4.69 | 4.59 | 4.69 | 4.71 | 4.69 | 4.69 | 4.59 | 4.664 | 0.051683 | 0.12 | -6.72
6 | 5.6 | 5.6 | 5.6 | 5.6 | 5.5 | 5.62 | 5.5 | 5.5 | 5.62 | 5.5 | 5.564 | 0.055618 | 0.12 | -7.26667
7 | 7.33 | 7.45 | 7.34 | 7.44 | 7.33 | 7.33 | 7.45 | 7.33 | 7.43 | 7.36 | 7.379 | 0.055668 | 0.12 | 5.414286
8 | 8.36 | 8.34 | 8.24 | 8.24 | 8.24 | 8.24 | 8.36 | 8.24 | 8.36 | 8.24 | 8.286 | 0.059666 | 0.12 | 3.575
9 | 8.93 | 9.02 | 8.91 | 9.03 | 8.93 | 9.02 | 8.91 | 9.02 | 8.91 | 9.02 | 8.97 | 0.055377 | 0.12 | -0.33333
10 | 10.24 | 10.24 | 10.34 | 10.34 | 10.34 | 10.22 | 10.34 | 10.33 | 10.33 | 10.33 | 10.305 | 0.049944 | 0.12 | 3.05
20 | 20.86 | 20.86 | 20.86 | 20.84 | 20.84 | 20.84 | 20.74 | 20.74 | 20.74 | 20.84 | 20.816 | 0.053166 | 0.12 | 4.08
30 | 30.28 | 30.28 | 30.28 | 30.28 | 30.38 | 30.38 | 30.29 | 30.28 | 30.28 | 30.28 | 30.301 | 0.041753 | 0.1 | 1.003333
40 | 40.21 | 40.21 | 40.21 | 40.21 | 40.22 | 40.12 | 40.1 | 40.12 | 40.1 | 40.21 | 40.171 | 0.053009 | 0.12 | 0.4275
50 | 49.24 | 49.24 | 49.24 | 49.24 | 49.24 | 49.26 | 49.26 | 49.26 | 49.34 | 49.36 | 49.268 | 0.044422 | 0.12 | -1.464
60 | 59.19 | 59.29 | 59.07 | 59.29 | 59.19 | 59.29 | 59.71 | 59.28 | 59.29 | 59.07 | 59.267 | 0.178889 | 0.64 | -1.22167
70 | 69.12 | 69.12 | 69.12 | 69.12 | 69.21 | 69.22 | 69.12 | 69.22 | 69.12 | 69.21 | 69.158 | 0.049171 | 0.1 | -1.20286
80 | 79.05 | 79.36 | 79.06 | 79.05 | 79.35 | 79.45 | 78.53 | 79.36 | 78.97 | 78.93 | 79.111 | 0.278147 | 0.92 | -1.11125
90 | 89.38 | 89.36 | 89.36 | 89.4 | 89.29 | 89.4 | 89.36 | 89.38 | 89.36 | 89.48 | 89.377 | 0.047621 | 0.19 | -0.69222
100 | 99.31 | 99.43 | 99.41 | 99.33 | 99.41 | 99.33 | 99.31 | 99.47 | 99.33 | 99.41 | 99.374 | 0.057966 | 0.16 | -0.626
150 | 150.34 | 150.28 | 150.69 | 150.38 | 150.36 | 150.36 | 150.81 | 150.38 | 150.78 | 150.38 | 150.476 | 0.200344 | 0.53 | 0.317333
200 | 199.1 | 199.12 | 199.1 | 198.69 | 198.6 | 199.12 | 199.14 | 199.12 | 198.74 | 199.05 | 198.978 | 0.211912 | 0.54 | -0.511
250 | 249.47 | 249.64 | 249.78 | 249.48 | 250.29 | 249.34 | 249.4 | 249.78 | 249.31 | 249.69 | 249.618 | 0.292567 | 0.98 | -0.1528
300 | 1124.55 | 1124.65 | 1126.45 | 1126.45 | 1126.55 | 1126.56 | 1124.45 | 1124.45 | 1124.67 | 1124.89 | 1125.367 | 0.985743 | 2.11 | 275.1223
 |  |  |  |  |  |  |  |  |  |  |  | 0.139551 | 0.36125 | 27.18571
 |  |  |  |  |  |  |  |  |  |  |  | 0.09427 | 0.265238 | 2.14519
From the data to the side, we can conclude a lot of things but the most important things we need to focus is that the data matches the data sheet at the beginning of this section
28

## Slide 29
Conclusion
The sensors were not up to industry standard but they do what they are supposed to do and this here we come in – to make up for that gap with our time and effort .
The sensors are not that crappy and we lost time focusing on that but at the end of the day we realized what we had to do!
29

## Slide 30
Thank You
Q/A
30